## Slide 1: Cache basic example
Chen-Hsiung Liu
2024/5/18

## Slide 2: Cache basic example
Assume cache architecture as following
Cache line is 64 Bytes
Depth of cache is 1024 entries
Use 32-bit address
2-way set-associative
With valid bit and dirty bit
Cache replacement policy is LRU (least recently used)
Initialize whole cache SRAM as 0 (represent as blank)

## Slide 3
Set | LRU | V0 | D0 | Tag0 | Data0 (64Bytes) | V1 | D1 | Tag1 | Data1 (64Bytes)
0 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
1023 |  |  |  |  |  |  |  |  | 
Requested Memory Address (32b) |  | 
Tag (16b) | Index (10b) | Offset (6b)
==
==
Miss/Hit
Encoder
Data (64B)
R Addr=0x12340080
R Addr=0x12350080
W Addr=0x12340084
R Addr=0x12360080

## Slide 4
Requested Memory Address (32b) |  | 
Tag (16b) | Index (10b) | Offset (6b)
==
==
Miss
Encoder
R 0x12340080
=
16'h1234
10'h2
6'h0
16'h1234
10'h2
6'h0
Set | LRU | V0 | D0 | Tag0 | Data0 (64Bytes) | V1 | D1 | Tag1 | Data1 (64Bytes)
0 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
1023 |  |  |  |  |  |  |  |  | 
0
0
1
0
0x..FEDCBA98
1
0x1234

## Slide 5
Requested Memory Address (32b) |  | 
Tag (16b) | Index (10b) | Offset (6b)
==
==
Miss
Encoder
R 0x12350080
=
16'h1235
10'h2
6'h0
16'h1235
10'h2
6'h0
Set | LRU | V0 | D0 | Tag0 | Data0 (64Bytes) | V1 | D1 | Tag1 | Data1 (64Bytes)
0 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
1023 |  |  |  |  |  |  |  |  | 
1
0
0
0x..FEDCBA98
1
0x1234
1
0
0x..CAFEBEEF
0x1235
0

## Slide 6
Requested Memory Address (32b) |  | 
Tag (16b) | Index (10b) | Offset (6b)
==
==
Hit
Encoder
W 0x12340084
=
16'h1234
10'h2
6'h4
16'h1234
10'h2
6'h4
Set | LRU | V0 | D0 | Tag0 | Data0 (64Bytes) | V1 | D1 | Tag1 | Data1 (64Bytes)
0 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
1023 |  |  |  |  |  |  |  |  | 
1
1
0
0x..FEDCBA98
0
0x1234
0
0x..CAFEBEEF
0x1235
1
0x..C0DEBA98
1

## Slide 7
Requested Memory Address (32b) |  | 
Tag (16b) | Index (10b) | Offset (6b)
==
==
Miss
Encoder
R 0x12360080
=
16'h1236
10'h2
6'h0
16'h1236
10'h2
6'h0
Set | LRU | V0 | D0 | Tag0 | Data0 (64Bytes) | V1 | D1 | Tag1 | Data1 (64Bytes)
0 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
1023 |  |  |  |  |  |  |  |  | 
1
1
1
0x..C0DEBA98
1
0x1234
0
0x..CAFEBEEF
0x1235
0x..FACEFEED
0
0x1236

## Slide 8: Reference
https://cs.nyu.edu/~gottlieb/courses/2000s/2007-08-fall/arch/lectures/lecture-22.html
https://www.cs.swarthmore.edu/~kwebb/cs31/f18/memhierarchy/caching.html
https://diveintosystems.org/book/C11-MemHierarchy/caching.html