## Slide 1: Cache Miss Rate Note
Chen-Hsiung Liu
2020/2/15

## Slide 2
Case 1: sequential read

## Slide 3: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 4 Bytes
8-way set associative
4 sets
Access pattern: (Read total 256 Bytes)
Read size is 4 Bytes
Read address 0x0 ~ 0xFF
Read burst length is 64
Cache miss 64 times
 |  | Way |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
40 | 44 | 48 | 4C | 50 | 54 | 58 | 5C
60 | 64 | 68 | 6C | 70 | 74 | 78 | 7C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC
C0 | C4 | C8 | CC | D0 | D4 | D8 | DC
E0 | E4 | E8 | EC | F0 | F4 | F8 | FC

## Slide 4: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 8 Bytes
4-way set associative
4 sets
Access pattern: (Read total 256 Bytes)
Read size is 4 Bytes
Read address 0x0 ~ 0xFF
Read burst length is 64
Cache miss 32 times, hit 32times (miss, hit, miss, hit, …)
 |  | Way |  |  |  |  |  |  | 
 |  | 0 |  | 1 |  | 2 |  | 3 | 
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
40 | 44 | 48 | 4C | 50 | 54 | 58 | 5C
60 | 64 | 68 | 6C | 70 | 74 | 78 | 7C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC
C0 | C4 | C8 | CC | D0 | D4 | D8 | DC
E0 | E4 | E8 | EC | F0 | F4 | F8 | FC

## Slide 5
Case 2: separate read

## Slide 6: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 4 Bytes
8-way set associative
4 sets
Access pattern: (Read total 128 Bytes)
Read size is 4 Bytes
Read address 0x0, 0x20, 0x80, 0xA0, 0x4, 0x24, 0x84, …, 0x9C, 0xBC
Total 32 4-byte read
Cache miss 32 times
 |  | Way |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC

## Slide 7: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 8 Bytes
4-way set associative
4 sets
Access pattern: (Read total 128 Bytes)
Read size is 4 Bytes
Read address 0x0, 0x20, 0x80, 0xA0, 0x4, 0x24, 0x84, …, 0x9C, 0xBC
Total 32 4-byte read
Cache miss 16 times (miss x 4, hit x 4, miss x 4, hit x 4, …)
 |  | Way |  |  |  |  |  |  | 
 |  | 0 |  | 1 |  | 2 |  | 3 | 
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC
Notes: Addr 0x0 ~ 0xA0 cache miss. Addr 0x4 ~ 0xA4 cache hit. Addr 0x8 ~ 0xA8 cache miss. Addr 0xC ~ 0xAC cache hit.
Addr 0x10 ~ 0xB0 cache miss. Addr 0x14 ~ 0xB4 cache hit. Addr 0x18 ~ 0xB8 cache miss. Addr 0x1C ~ 0xBC cache hit.

## Slide 8: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 16 Bytes
2-way set associative
4 sets
Access pattern: (Read total 128 Bytes)
Read size is 4 Bytes
Read address 0x0, 0x20, 0x80, 0xA0, 0x4, 0x24, 0x84, …, 0x9C, 0xBC
Total 32 4-byte read
Cache miss 8 times (miss x 4, hit x 12, miss x 4, hit x 12)
 |  | Way |  |  |  |  |  |  | 
 |  | 0 |  |  |  | 1 |  |  | 
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC
Notes: Addr 0x0 ~ 0xA0 cache miss. Addr 0x4 ~ 0xAC cache hit. Addr 0x10 ~ 0xB0 cache miss. Addr 0x14 ~ 0xBC cache hit.

## Slide 9: Cache architecture (data sram)
Cache size is 128 Bytes
Cache line is 32 Bytes
1-way set associative (direct map)
4 sets
Access pattern: (Read total 128 Bytes)
Read size is 4 Bytes
Read address 0x0, 0x20, 0x80, 0xA0, 0x4, 0x24, 0x84, …, 0x9C, 0xBC
Total 32 4-byte read
Cache miss 32 times
 |  | Way |  |  |  |  |  |  | 
 |  | 0 |  |  |  |  |  |  | 
Set | 0 |  |  |  |  |  |  |  | 
 | 1 |  |  |  |  |  |  |  | 
 | 2 |  |  |  |  |  |  |  | 
 | 3 |  |  |  |  |  |  |  | 
0 | 4 | 8 | C | 10 | 14 | 18 | 1C
20 | 24 | 28 | 2C | 30 | 34 | 38 | 3C
80 | 84 | 88 | 8C | 90 | 94 | 98 | 9C
A0 | A4 | A8 | AC | B0 | B4 | B8 | BC
(anime only show access 0x0 ~ 0xA4)
Notes: Create anime is sooooo tired.

## Slide 10: Cache miss rate
According to case 2 separate read
Chart: Cache miss rate
| 8-way | 4-way | 2-way | 1-way
case 2 | 1 | 0.5 | 0.25 | 1