## Slide 1: SystemVerilog parser Introduction
Chen-Hsiung Liu
2020/9/25

## Slide 2: Agenda
Introduce SystemVerilog parser tools and comparison
Demo examples.

## Slide 3: Choice of SystemVerilog parser (1/3)
https://github.com/chipsalliance/sv-tests
Test suite to check compliance with the SystemVerilog standard.

## Slide 4: Choice of SystemVerilog parser (2/3)
Detail test report

## Slide 5: Choice of SystemVerilog parser (3/3)
First, verible-verilog-syntax
  Pass 94% syntax in 5s and use only 14MB memory.
  Best performance over 690KB/s
Second, Slang
  The only one pass 100% SV syntax.
  Use 42s and 105MB memory, performance not so good.
  For accurate SV syntax check.

## Slide 6: Run slang with example online
Slang explorer (inspired by Compiler Explorer)
`pragma protect directives are validated for correctness.
encrypted text is skipped
Notes: module dut ();
wire sig_a;
wire sig_b;
wire [3:0] sig_c;
wire sig_d;
endmodule
module tb;
dut dut();
`define HIER tb.dut
logic dbg_a;
logic [3:0] dbg_b;
logic dbg_c;
assign dbg_a = `HIER.sig_a;
assign dbg_b = `HIER.sig_b;
assign dbg_c[3:0] = `HIER.sig_c[3:0];
logic dbg_a;
assign dbg_a = `HIER.sig_d;
endmodule

## Slide 7: Run slang with UVM example on Linux
UVM example with errors

## Slide 8: UVM example source
`uvn_field_string in basic_item is incorrect.
Use req.data out of bounds.

## Slide 9: Default options
Use these option to skip not caring errors and warnings

## Slide 10: Performance comparison
--lint-only Only perform linting of code, don't try to elaborate a full hierarchy.
 | Simulator | Slang
Case 1 | 4.94s 0 warnings | 0.15s (33x) 0 errors, 0 warnings
Case 2 | 60s 17 warnings | 1.49s (40x) 12 errors, 3 warnings
Case 3 | 225s 3367 warnings | 17.19s (13x) 99 errors, 3325 warnings
Case 4 | 190s 619 warnings | 49.87s (3.8x) 1337 errors, 11585 warnings
 |  | 22.93s (8x) lint-only 874 errors, 10043 warnings