## Slide 1: UVM TLM Introduction
Chen-Hsiung Liu
2024/10/27

## Slide 2: UVM Testbench Architecture
Notes: https://csbearnokiseki.blogspot.com/2017/06/uvm.html

## Slide 3: Communication in UVM: TLM 1.0, 2.0
TLM Classes – 1.0
  uvm_*_port
  uvm_*_export
  uvm_*_imp
  uvm_*_fifo
TLM Classes – 2.0
  uvm_*_socket
env
sequencer
driver
sequence

## Slide 4: UVM TLM 1.0
Push
Pull
Fifo
Analysis (broadcast)
put_producer calls port.put()
put_consumer implements put()
pull_consumer implements pull()
pull_producer calls port.pull()
producer calls port.put()
consumer calls port.pull()
write_producer calls port.write()
write_subscriber implements write()
FIFO
write_subscriber implements write()
write_subscriber implements write()

## Slide 7
virtual function bit can_*()
Returns 1 if a new transaction is available; 0 otherwise.
Class \ Method | put | try_ put | can_ put | get | try_ get | can_ get | peek | try_ peek | can_ peek | write
uvm_blocking_ put_port | X |  |  |  |  |  |  |  |  | 
uvm_nonblocking_ put_port |  | X | X |  |  |  |  |  |  | 
uvm_put_port | X | X | X |  |  |  |  |  |  | 
uvm_blocking_ get_port |  |  |  | X |  |  |  |  |  | 
uvm_nonblocking_ get_port |  |  |  |  | X | X |  |  |  | 
uvm_get_port |  |  |  | X | X | X |  |  |  | 
uvm_blocking_ peek_port |  |  |  |  |  |  | X |  |  | 
uvm_nonblocking_ peek_port |  |  |  |  |  |  |  | X | X | 
uvm_peek_port |  |  |  |  |  |  | X | X | X | 
uvm_blocking_ get_peek_port |  |  |  | X |  |  | X |  |  | 
uvm_nonblocking_ get_peek_port |  |  |  |  | X | X |  | X | X | 
uvm_get_peek_port |  |  |  | X | X | X | X | X | X | 
uvm_blocking_ master_port | X |  |  | X |  |  | X |  |  | 
uvm_nonblocking_ master_port |  | X | X |  | X | X |  | X | X | 
uvm_master_port | X | X | X | X | X | X | X | X | X | 
uvm_blocking_ slave_port | X |  |  | X |  |  | X |  |  | 
uvm_nonblocking_ slave_port |  | X | X |  | X | X |  | X | X | 
uvm_slave_port | X | X | X | X | X | X | X | X | X | 
uvm_analysis_port |  |  |  |  |  |  |  |  |  | X
TLM Port methods

## Slide 10: UVM TLM FIFO
default size = 1
default size = 0, unbounded
(uvm_analysis_imp)

## Slide 11: TLM connect
Hierarchical port connections are resolved and optimized just before uvm_component::end_of_elaboration_phase. After optimization, calling any port’s interface method (e.g. leaf1.out.put(trans)) incurs a single hop to get to the implementation (e.g. leaf2’s put task), no matter how far up and down the hierarchy the implementation resides.
port-to-port | leaf1’s out port is connected to its parent’s (comp1) out port
port-to-export | comp1’s out port is connected to comp2’s in export
export-to-export | comp2’s in export is connected to its child’s (subcomp2) in export
export-to-imp | subcomp2’s in export is connected leaf2’s in imp port.
imp-to-implementation | leaf2’s in imp port is connected to its implementation, leaf2

## Slide 13: Port Base Class
uvm_port_base #(IF)
The debug_connected_to method outputs a visual text display of the port/export/imp network to which this port connects (i.e., the port’s fanout).
The debug_provided_to method outputs a visual display of the port/export network that ultimately connect to this port (i.e., the port’s fanin).

## Slide 14
Check and Debug Connection

## Slide 15: UVM built-in check
Size check uses size() to get the number of implementation ports connected to this port.
`UVM_PORT_COMMON, `UVM_EXPORT_COMMON, `UVM_IMP_COMMON, default min_size=1, max_size=1.
uvm_analysis_port, default min_size=0, max_size=unbounded.
uvm_analysis_export, default min_size=1, max_size=unbounded.
uvm_analysis_imp, default min_size=1, max_size=1.
Error message example:
[Connection Error] connection count of 0 does not meet required minimum of 1
[Connection Error] connection count of 2 exceeds maximum of 1

## Slide 16: TLM Connection Example (1)
This is legal.
env
compA1
compB1
subcompA
subcompB
compA2
compB2
subcompA
subcompB

## Slide 17: TLM Connection Example (2)
This is legal.
env
compA1
compB1
subcompA
subcompB
compA2
compB2
subcompA
subcompB

## Slide 18: TLM Connection Example (3)
This is illegal.
env
compA1
compB1
subcompA
subcompB
compA2
compB2
subcompA
subcompB

## Slide 19: TLM Connection Example (4)
This is legal. (not recommended)
env
agent
scoreboard
monitor
uvm_tlm_analysis_fifo
analysis_export
get()

## Slide 20: UVM TLM 2.0
Blocking
Non-blocking
initiator
target
b_transport (tx, delay)
initiator
target
nb_transport_fw (tx, p, delay)
nb_transport_bw (tx, p, delay)

## Slide 21: TLM 2.0 Generic Payload